## Slide 1: IoT Device Fingerprinting on Commodity Switches Carson Kuzniar, Miguel Neves, Vladimir Gurevich, Israat Haque
1

## Slide 2: IoT Landscape
2
12.3 billion connected IoT devices ​
Roughly $160 Billion in IoT enterprise spending​
IoT botnet-based DDoS attacks reaching over 1 Tbps
Hundreds of thousands of compromised devices
  Above 200K for Mirai botnet

## Slide 3: IoT Fingerprinting
3
Critical task for network administrators to
    Check for known vulnerabilities
    Set access/firewall rules
    Configure intrusion detection systems

## Slide 4: State of the Art
4
Machine Learning (WiSec’20)
Labeled Traffic from Manufacture/User (NOMS’20)
Length and direction-based signatures (NDSS’20, IM’21)
Solutions face obstacles at scale or with network wide view
Require mirroring traffic to dedicated hardware

## Slide 5: Device Signatures
5
Use packet length and direction to create signatures for events (e.g., On/Off)
Reliably fingerprint devices using these signatures
R. Trimananda, J. Varmarken, A. Markopoulou, and B. Demsky, “Packet-Level Signatures for Smart Home Devices,” Proceedings of the 2020 Network and Distributed System Security (NDSS) Sympo- sium, February 2020.

## Slide 6: Challenges
6
    Volume
    Large amounts of traffic on high-speed links
    Drop accuracy or add significant delay

## Slide 7: Challenges
7
    Volume
    Large amounts of traffic on high-speed links
    Drop accuracy or add significant delay
    Granularity
    Sampling and aggregation miss quiet device

## Slide 8: Introducing PoirIoT
8
Programmable Data-Plane based Fingerprinting:
High-speed : Tofino ASIC Line Rate (Tbps)
High granularity: Inspects every packet as part of its forwarding process
Modular : Efficient use of switch resources

## Slide 9: PoirIoT Architecture
9

## Slide 10: PoirIoT Architecture
10

## Slide 11: Signature Extraction
11

## Slide 12: Signature Extraction
12

## Slide 13: Signature Extraction
13

## Slide 14: Signature Extraction
14

## Slide 15: Signature Extraction
15

## Slide 16: PoirIoT Architecture
16

## Slide 17: DFA and Rule Creation
17

## Slide 18: DFA and Rule Creation
18

## Slide 19: DFA and Rule Creation
19

## Slide 20: PoirIoT Architecture
20

## Slide 21: PoirIoT Data Plane
21

## Slide 22: PoirIoT Data Plane
22
State and Timer info stored per flow
Virtual FSM per flow while requiring only a single table

## Slide 23: PoirIoT Data Plane
23
State and Timer info stored per flow
Virtual FSM per flow while requiring only a single table

## Slide 24: PoirIoT Data Plane
24
Length filter prevents resource allocation to flows with no packets of interest

## Slide 25: PoirIoT Data Plane
25
Resubmit used instead of recirculation to update information without costs of engaging traffic manager

## Slide 26: Evaluation
26
PoirIoT implemented on Wedge 100BF-32X with Tofino ASIC
Code Available (https://github.com/PINetDalhousie/poiriot)
IoT traffic from publicly available dataset
14 devices
~30 Signatures
More results/details in Paper

## Slide 27: Device Detection
27
Detect all 14 devices
Timeouts needs to be sufficiently long to allow for RTT and longer signatures

## Slide 28: Device Detection
28
Detect all 14 devices
Timeouts needs to be sufficiently long to allow for RTT and longer signatures

## Slide 29: Device Detection
29
Two types of synthetic signatures: uniformly sampled or derived from existing signature set
Detection accuracy remains high (80%+) with hundreds of additional signatures

## Slide 30: Device Detection
30
Two types of synthetic signatures: uniformly sampled or derived from existing signature set
Detection accuracy remains high (80%+) with hundreds of additional signatures

## Slide 31: Scalability
31
Switch memory supports 200,000 signatures or 400,000 connections
WIDE Trace shows flows the have a packet length matching one of our initial lengths

## Slide 32: Scalability
32
Switch memory supports 200,000 signatures or 400,000 connections
WIDE Trace shows flows the have a packet length matching one of our initial lengths

## Slide 33: Resource Consumption
33
Application takes minimal amounts of switch resources (No TCAM at all)
SRAM most consumed resource (stateful information + table entries)
Resource | Usage
Match Crossbar | 3.1%
SRAM | 5.1%
TCAM | 0%
VLIW Instruction | 3.4%
Hash Bits | 4.7%

## Slide 34: Resource Consumption
34
Application takes minimal amounts of switch resources (No TCAM at all)
SRAM most consumed resource (stateful information + table entries)
Resource | Usage
Match Crossbar | 3.1%
SRAM | 5.1%
TCAM | 0%
VLIW Instruction | 3.4%
Hash Bits | 4.7%

## Slide 35: Resource Consumption
35
Application takes minimal amounts of switch resources (No TCAM at all)
SRAM most consumed resource (stateful information + table entries)
Resource | Usage
Match Crossbar | 3.1%
SRAM | 5.1%
TCAM | 0%
VLIW Instruction | 3.4%
Hash Bits | 4.7%

## Slide 36: Summary
36
State of the art fingerprinting solutions face challenges (volume and granularity) at scale
PoirIoT brings fingerprinting to data plane offering:
System consists of two components controller + switch data plane
Solution detects 100% of devices in a publicly available data set while using minimal switch resources
High Speed
Packet level granularity

## Slide 37
37
Questions?
Carson Kuzniar
carson.kuzniar@dal.ca

## Slide 38: References
38
A. Acar, H. Fereidooni, T. Abera, A. K. Sikder, M. Miettinen, H. Aksu, M. Conti, A.-R. Sadeghi, and S. Uluagac, “Peek-a-boo: I see your smart home activities, even encrypted!” in Proceedings of the 13th ACM Conference on Security and Privacy in Wireless and Mobile Networks, ser. WiSec ’20, 2020, p. 207–218.
Y. Afek, A. Bremler-Barr, D. Hay, R. Goldschmidt, L. Shafir, G. Avraham, and A. Shalev, “Nfv-based iot security for home networks using mud,” in NOMS 2020 - 2020 IEEE/IFIP Network Operations and Management Symposium, 2020, pp. 1–9
R. Trimananda, J. Varmarken, A. Markopoulou, and B. Demsky, “Packet-Level Signatures for Smart Home Devices,” Proceedings of the 2020 Network and Distributed System Security (NDSS) Sympo- sium, February 2020.
C. Duan, S. Zhang, J. Yang, Z. Wang, Y. Yang, and J. Li, “Pin- ball: Universal and robust signature extraction for smart home devices,” in 2021 IFIP/IEEE International Symposium on Integrated Network Management (IM), 2021, pp. 1–9.

## Slide 39: Server Vs Switch
39
Server drops packets at high rates and misses events
Switch operates at line rate so no degradation as rates increase

## Slide 40: Event Detection
40
Event accuracy starts to decrease at longer timeouts because of a lack of resets
Event detection more granular so suffers more as signatures are added